## Slide 1
AeroSniffer
XIAO ESP32S3 Multi-Boot Desk Gadget
DeskBuddy 2.0 Kit Build | v2.0
By aryancodesit

## Slide 2
What is AeroSniffer?
Three separate devices in one tiny XIAO ESP32S3 chipMode 1: The Companion — Interactive desk pet with animated eyesMode 2: Network Auditor — 802.11 sniffer + web UI control panelMode 3: Flight Radar — Live ADS-B tracker from OpenSky NetworkInstant mode switching via 1.5s long-press on touch sensorBuilt on FreeRTOS dual-core architecture (Core 0: data, Core 1: UI)

## Slide 3
Hardware: DeskBuddy 2.0 Kit
One purchase. Everything included. Rs 2,299.
Component | Specification
Microcontroller | Seeed XIAO ESP32S3 (8MB Flash, 8MB PSRAM)
Display | 1.3" ST7789 240x240 Square IPS (SPI)
Touch Input | Red Capacitive Touch Switch Module
Battery | 3.7V LiPo (matched to enclosure)
Enclosure | 3D Printed Shell (pre-made)
Extras | On/Off switch + USB-C cable

## Slide 4
Wiring — Only 10 Wires!
Module | XIAO Pins | GPIO #
TFT MOSI | D10 | GPIO 9
TFT SCLK | D8 | GPIO 7
TFT CS | D3 | GPIO 4
TFT DC | D2 | GPIO 3
TFT RST | D9 | GPIO 8
Touch SIG | D0 | GPIO 1
VCC + GND | 3V3 + GND | (x2 modules)

## Slide 5
Mode 1: The Companion
Interactive desktop pet with OLED-style animated eyesTouch Sensor: Tap the roof to "pet" it — triggers happy expressionEmotions: Idle, Happy, Blink, Sleeping (auto-cycles)Blush marks, glare dots, and smooth smile arcsFace perfectly centered on the 240x240 square displayLong-press (1.5s) on touch sensor = switch to Mode 2

## Slide 6
Mode 2: Security Monitor
Web-UI Hybrid Architecture (optimized for 1.3" screen)ON SCREEN: Animated radar sweep + live PKT/s bar + statsON PHONE: Connect to "AeroSniffer-SEC" WiFi APWeb UI at http://192.168.4.1 — start/stop scans, view packetsPromiscuous 802.11 capture with channel hoppingDeauth spike alerting (>10 frames in 5s = ALERT)Companion desktop app (planned) for USB Serial control

## Slide 7
Mode 3: Flight Radar
Live ADS-B flight tracker via OpenSky Network APIConnects to home WiFi (STA mode) — polls every 15sCompact flight cards: callsign, altitude, speed, headingMini compass rose + radar dot-map on each cardAuto-scrolls through detected flights in your areaCustomizable GPS bounding box in Config.h

## Slide 8
DeskBuddy 2.0 Enclosure
Pre-made 3D-printed shell — included in the kitUltra-compact form factor (XIAO is 21mm x 17.5mm!)Display window: pre-cut for 1.3" ST7789 moduleTouch sensor: mounted under the roof for head-patsUSB-C slot: access port for charging and firmware updatesBattery compartment: sized for the included LiPo cellLooks like a premium consumer product on your desk

## Slide 9
Software Setup
IDE: Arduino IDE 2.xBoard: XIAO_ESP32S3 (esp32 by Espressif Systems v3.0.x+)Settings: 8MB Flash, OPI PSRAM, USB CDC On Boot: EnabledRequired Libraries: TFT_eSPI (display) + ArduinoJson (API)Only 2 libraries needed! (mic/DAC/IMU not wired = not needed)

## Slide 10
Configuration — 2 Easy Steps
1. Copy TFT_eSPI_UserSetup.h → Arduino/libraries/TFT_eSPI/User_Setup.h Pre-configured for ST7789 240x240 + XIAO SPI pins2. Edit Config.h: Set WIFI_SSID and WIFI_PASSWORD Set GPS bounding box (boundingbox.klokantech.com) Hardware variant HW_DESKBUDDY_2 is already selected

## Slide 11
Flash & Test
Step 1: Upload SPIFFS data (airlines.db) via LittleFS pluginStep 2: Open AeroSniffer.ino → Click UploadStep 3: Boot splash appears → Mode 1 (Pet) loadsStep 4: Tap touch sensor → pet goes happy!Step 5: Long-press (1.5s) → cycles through all 3 modesIf upload fails: Hold BOOT → Press RESET → Release BOOT

## Slide 12
Companion App (Planned)
Web app (Vercel) or desktop .exe — connects via USB SerialFull Marauder control panel when device is plugged inFirmware update checker and OTA capabilityBuilt-in how-to tutorial and payload libraryReal-time packet visualization and export

## Slide 13
Software Architecture
FreeRTOS dual-core task routing: Core 0: Background — WiFi, packet capture, API fetch Core 1: UI Engine — TFT rendering, touch polling, state machineFeature flags (#if HAS_MIC, HAS_DAC, etc.) for optional hardwareDual hardware profiles: HW_DESKBUDDY_2 and HW_DEVKITCClean mode teardown/setup — no reboot needed between modes

## Slide 14
Questions?
Enjoy your AeroSniffer!
github.com/aryancodesit/AeroSniffer
Built on DeskBuddy 2.0 Kit | Rs 2,299 | esclabs.in